# Nokia 6020 LCD

Parameter	Nokia 6020
Type	active-matrix TFT
Connector	12 pin Hirose DF23C-12DS-0.5
Controller	Philips PCF8833
Resolution	130×130 pixels
Visible resolution	128×128 pixels
Native colors	65536 (16 bit)
Supported colors	256 (8 bit), 4096 (12 bit), 65536 (16 bit)
Color format	RGB
Interface	9 bit SPI

To connect to LCD you need 12 pin “Hirose DF23C-12DS-0.5” connector (receptacle).
Looking from the back pinout is the following:

Pin number	Symbol	Description
1	LED-	minus for display backlight
2	VDDI	Voltage supply (1.65V – 1.95V)
3	GND	System ground
4	SDA(MOSI)	Serial input
5	CSX	Chip select (active low)
6	GND	System ground
7	NC	not connected
8	RESX	Reset (active low)
9	SCL(SCLK)	Serial input clock
10	GND	System ground
11	VDD	Voltage supply (2.6V – 2.9V)
12	LED+	plus for display backlight

I didn’t find out any information about how much voltage difference between LED- and LED+ is needed for backlight. I tried 6.6V and it is not enough. With 10V the backlight works.
https://kbiva.wordpress.com/2013/07/25/nokia-6020-lcd/